Subject:	Description of the Wood Packaging Marking Programme of the Netherlands

Date:		April 2004

Reference:	TRCPD/2003/2114

Author:	Bram de Hoop

###### 1. Purpose

This information note serves to inform other countries of the Wood Packaging Marking Programme of the Netherlands. This marking programme is aimed at ensuring compliance with import regulations for wood packaging material of other countries in line with requirements of ISPM 15. The marking programme was set up in the course of 2002 and 2003 in consultation with organised industry and experts in certification.

On the first of October 2003 the first companies (treatment facilities, manufacturers, repair companies, traders) in the Netherlands have been certified by the Netherlands Plant Protection Service, for using the IPPC mark (see figure 1). Approximately 60 companies have been registered and are certified to use the ISPM 15 mark, in April 2004. Certified companies can manufacture wood packaging material, which has undergone heat treatment  and can apply the IPPC mark in accordance with ISPM 15.

Figure 1:	 The IPPC mark (see ISPM 15 http://www.ippc.int/IPP/En/default.htm) as authorised by the Netherlands Plant Protection Service for use by certified companies. The only variable concerns 00 = unique number assigned tothe producer of the wood packaging material.

2. Summary

The Netherlands Plant Protection Service is responsible for setting preconditions to the programme, formal approval of certified companies and audit of the marking programme. Administration of the programme has been assigned by contract agreement to an independent organisation (SMHV = Stichting Markering Houten Verpakkingen). The organisation is responsible for national communication, set-up and maintenance of a registration information system, development of inspection protocols, admission and suspension of companies to the programme. Inspections for determining compliance of companies with inspection protocols is performed by an independent inspection agency (SGS Agrocontrol), which will be accredited in the Netherlands for this purpose. Prosecution of companies who make misuse of the IPPC mark is the responsibility of the authorities of the Netherlands.

3. Tasks of the Netherlands Plant Protection Service

Compliance with ISPM 15 treatment requirements cannot be determined by inspection or testing of the final product concerned. Therefore the most important precondition set by the Netherlands Plant Protection Service concerns inspection of the entire production process (including treatment), storage and admin of the company concerned by inspection agencies which will be accredited for this specific application in line with ISO requirements.  Next to setting preconditions to the programme, the Netherlands Plant Protection Service is responsible for international communication concerning pest risk and requirements for import posed by other countries in relation to the programme. The Netherlands Plant Protection Service will audit the programme by verifying accreditation reports of SGS Agrocontrol and by audit visits to SMHV and SGS Agrocontrol. In addition ad-hoc visits for inspection of the production process and admin arrangements of registered companies will be undertaken during the first year as an additional check.

3. Pest risk communication
The highest level of phytosanitary safeguards for compliance with ISPM 15 requirements is provided by wood packaging material, which has been manufactured or repaired by companies which have been admitted to the programme. In line with ISPM 15, the Netherlands Plant Protection Service allows use of recirculating wood packaging material with proof or mark indicating proper treatment.

4. Tasks of the SMHV (Stichting Markering Houten Verpakkingen – See http://www.smhv.nl/)
The SMHV is the most important organisation within the marking programme and responsible for set-up and maintenance of inspection protocols, registration, admission and suspension of companies from the programme, resolution of disputes and national communication. For ensuring technical and administrative competency, the organisation has set up an advisory committee with representatives of manufacturers, traders, treatment experts, and the logistics industry. Next to auditing the SMHV, the Netherlands Plant Protection Service also partakes in committee meetings to provide advice on international developments and national regulatory aspects.

5. Tasks of the inspection agency SGS Agrocontrol (see http://www.sgs.nl/contact.asp)
A specialised inspection agency with experience in certification and inspection of companies producing wood related products has been hired by SMHV. The inspection agency is responsible for inspections in order to allow admission of interested companies to the programme. In addition the inspection agency will undertake two ad-hoc visits for each company, each year, in order to verify compliance.

6. Registered Companies in the Netherlands
A list of registered companies can be provided on request or attained from the website of SMHV (see item 4 of this information note). Registered companies include manufacturers, traders and repair companies of wood packaging material, next to companies operating treatment facilities or trading wood. For the production of wood packaging material, companies may also use wood treated in line with ISPM 15 requirements, imported from other countries. This is only possible for countries whereby the concerned NPPO has communicated a description of its verification programme to ensure compliance with heat treatment requirements of sawmills. As a minimum NPPOs should indicate in what way heat treatment capacities of sawmills are verified and NPPOs should communicate an updated list of approved sawmills in their country. Wood coming from registered companies in inter alia Finland, Latvia, Norway, Poland and Sweden can be used by companies in the Netherlands for manufacturing and marking wood packaging material with the IPPC mark, as part of the Netherlands wood packaging marking programme.

7. Further information

For further information please contact:

Bram de Hoop
Official IPPC Contact point of the Netherlands

Tel: +31 317 496629
Email: m.b.de.hoop@minlnv.nl

# Text boxes

### NL – 00

HT  DB