12 July 2011

# GLOBAL EQUIPMENT CLEANING GUIDELINES

# GLOBAL EQUIPMENT CLEANING GUIDELINES

1.	GENERAL STATEMENT OF CLEANLINES	2

2.	CLEANING CRITERIA	3

2.1.	INTRODUCTION	3

2.2.	CLEANING CRITERIA TABLE FOR DRY CONTAINERS	4

2.3.	CLEANING CRITERIA TABLE FOR REEFER CONTAINERS	5

2.4.	CLEANING CRITERIA – CONTAINERS THAT HAVE PREVIOUSLY     CONTAINED DANGEROUS, HAZARDOUS, POTENTIALLY DANGEROUS OR OBNOXIOUS CARGOES	6

3.	CLEANING METHODS	7

3.1.	INTRODUCTION	7

3.2.	PERSONAL PROTECTION EQUIPMENT	7

3.3.	GENERAL CLEANING METHODS	8

3.4.	SPECIFIC CLEANING METHODS	8

3.4.1.	Labels, Marks or Signs	8

3.4.2.	Dry Contamination (Debris or Dirt)	9

3.4.3.	Wet Contamination	9

3.4.4.	Infestation	10

3.4.5.	Paint Contamination	10

3.4.6.	Persistent Odour	10

3.4.7.	Liquids and Transferable Stains	11

3.4.8.	Condensation or Standing Water (and other miscellaneous wet conditions)	11

3.4.9.	Glue Residues	11

3.4.10.	Protruding Nails	12

3.4.11.	Graffiti	12

3.4.12.	Cargo Securing Devices including Tape	12

3.4.13.	Reefer Container Floor Drain holes	12

3.4.14.	Fumigation Residues	12

4.	DEFINITION OF TERMS	13

5.	MAERSK LINE CONTACTS FOR DANGEROUS RESIDUE INDENTIFICATION	14

6.	MAERSK LINE BASIC “FOOD GRADE” CONTAINER STANDARD DEFINITION	15

6.1.	Exterior Standard	15

6.2.	Interior Standard	15

6.3.	General Requirements	16

6.4.	Odours	16

6.5.	Costs for Upgrading Food Grade Containers	16

7.	MAERSK LINE CLEANING DEFINITIONS	17

7.1.	STS 0806 - Remove Nails	17

7.2.	STS 0910 – Food Grade (Only Oceania/France)	17

7.3.	STS 0912 – Cleaning in Excess of MCIC/MRIC	17

7.4.	STS 0914 - Internal Cleaning (Full Import/MTY Pos)	17

7.5.	STS 0918 - PARTIAL BLAST/REPAINT (ONLY GLBEMR'S APP)	17

7.6.	STS 0919 - MECHANICAL CLEAN (ONLY AFTER GLBEMR'S APP)	17

8.	MAERSK LINE STANDARD TIME SYSTEM CLEANING COSTS (Material+Time)	18

12 July 2011

# GENERAL STATEMENT OF CLEANLINES

This statement refers to the state of cleanliness of ALL containers used for the carriage of dry, special or reefer cargoes by sea.

Maersk Line requires that containers be returned in a clean condition, failure to do so may mean that the container will not be accepted or costs associated with subsequent cleaning will be charged to the previous shipper and/or consignee. This requirement is clearly specified and required in the Bill Of Lading contract:

“…If Containers supplied by or on behalf of the Carrier are unpacked by or for the Merchant, the Merchant is responsible for returning the empty Containers, with interiors clean, odour free and in the same condition as received, to the point or place designated by the Carrier, within the time prescribed. Should a Container not be returned in the condition required and/or within the time prescribed in the Tariff, the Merchant shall be liable for any detention, loss or expense incurred as a result thereof….”

It is imperative that no attempt is made to enter or clean a container until any residue has been identified and the appropriate cleaning instructions have been received. In case of doubt about how to treat residues proceeding from previous commodities, the Dangerous Cargo department of Maersk Line should be consulted for advice on the previous cargo and cleaning instructions.

A container shall be considered clean if there is no presence of:

- Dangerous cargo / IMDG labels, marks or signs.

- Loose soil, sand, mud, dirt, cargo residue, dunnage or other general rubbish.

- Infestation by animals, insects, fungi or any other living organism.

- Cargo securing devices such as metal or wire straps, cables, chains, string, rope etc…

- Tape plastic and/or any other material.

- Glue or adhesive or any other sticky material on walls, floor, ceilings etc.

- Nails bolts or any other fixing devices protruding above the level of the floor.

- Any persistent, obnoxious or unpleasant odour in the container that is liable to affect future cargoes.

- Marks, stains, or contaminations which are wet and/or transferable, including hydraulic fluid from cargo handling equipment.

- Loose sealant, internally in reefers.

See accompanying tables for specific criteria relating to container types.

A container will be considered unclean if there is presence of large amounts of dry glue, internal or external graffiti, adhesive or any other sticky material or other cargo related substances, which can be directly related to the previous shipper and/or consignee.

For reefer containers there should be no sign of organic residues or persistent odours from previous cargoes

The level of container cleanliness may be specified by the local Customer Service organisation to suit individual shippers' requirements.

# CLEANING CRITERIA

## INTRODUCTION

It is imperative that no attempt is made to enter or clean a container until it has been determined that it is safe to do so. Special care must be exercised where containers display Dangerous Cargo labels, marks or signs or the remnants of labels, marks or signs. Strong odours or unidentified residues may also indicate the presence of toxic or possibly toxic substances. When signs or traces of contamination are found or where there is any doubt about whether a residue is Dangerous or not the container should be closed and isolated and the Dangerous Cargo department of ML contacted to identify the residue and advise the appropriate cleaning instructions.

DO NOT ATTEMPT TO CLEAN UNTIL THE SUBSTANCE HAS BEEN IDENTIFIED AND APPROPRIATE CLEANING INSTRUCTIONS HAVE BEEN RECEIVED.

Reefer containers must not contain any kind of residue when released for packing. The normal clean for a reefer container is either a hot water wash or a steam-clean.

Appropriate precautions e.g. venting thoroughly, are to be taken before entry especially for Controlled or Modified Atmosphere (CA, MA) reefer containers as a low oxygen atmosphere may be present, never assume that the atmosphere is safe and vent unit before entering, however it is important to mention that low oxygen levels should have been ventilated during the unstuffing of the import cargo.

No material or agent may be used for the cleaning of containers that contains Chlorine, Phenol or any other chemical that could result in a residue liable to taint future cargoes. This is especially important for reefer containers, which are designed to carry foodstuffs.

## CLEANING CRITERIA TABLE FOR DRY CONTAINERS

| COMPONENT | CONDITION | ACTION REQUIRED | REFER TO SECTION |
| --- | --- | --- | --- |
| Interior And Exterior | Labels, marks or signs including Dangerous or potentially Dangerous | REMOVE | 3.2.1 |
|  | Contamination Dangerous or potentially Dangerous. | If condition could be threatening to human life or health container may be rejected at gate. Otherwise container must be segregated and Consignee or ML contacted to establish type of contaminant and appropriate action. Do not attempt to clean until instructions are received. | 3.2.2 or 3.2.3 or 3.2.6 |
|  | Graffiti: Racist comments or offensive language only. | REMOVE or OBLITERATE | 3.2.11 |
|  | Protruding nails | REMOVE | 3.2.10 |
| Interior | Soil, sand, mud or other loose residue or dirt in excess of that which would generally remain after a sweep out. | Should not be accepted by Depot if exhibiting these conditions. CLEAN | 3.2 or 3.2.2 |
|  | Patch (of any size) of sticky glue | REMOVE | 3.2.9 |
|  | Infestation | REMOVE & CLEAN | 3.2.4 |
|  | Persistent Odour | CLEAN & VENTILATE | 3.2.6 |
|  | Standing water | REMOVE | 3.2.8 |
|  | Organic residues e.g. Beans, grains, seeds etc. | REMOVE | 3.2 or 3.2.2 |
|  | Cargo securing devices such as metal or wire straps, cables, chains, string, and rope etc. including tape, subject to impinging into cube. | REMOVE | 3.2.12 |
|  | Graffiti: Racist comments or offensive language only. | REMOVE or OBLITERATE | 3.2.11 |
| Floors | Transferable stains but not including tyre marks. | If any single stain exceeds 25mm in diameter OR if 5 or more stains are dispersed with a single quadrant of floor surface area: CLEAN All transferable stains with liquids pooled above the floor surface or within a gouge: CLEAN | 3.2.7 3.2.7 |
|  | Protruding nails | REMOVE | 3.2.10 |

## CLEANING CRITERIA TABLE FOR REEFER CONTAINERS

The ML standard clean for a reefer container is either a high-pressure hot water wash or a steam clean. However reefer containers must be cleaned in accordance with local quarantine requirements before release for packing, even if they differ from these criteria.

| COMPONENT | CONDITION | ACTION REQUIRED | Refer to Section |
| --- | --- | --- | --- |
| Interior And Exterior | Labels, marks or signs, especially Dangerous or potentially Dangerous | REMOVE | 3.4.1 |
|  | Contamination (Dangerous or potentially Dangerous) | If condition could be threatening to human life or health container may be rejected at gate. Otherwise container must be segregated and Consignee or ML contacted to establish type of contaminant and appropriate action. Do not attempt to clean until instructions are received. | 3.4.2 or 3.4.3 |
|  | Graffiti: Racist comments or offensive language only | REMOVE or OBLITERATE | 3.4.11 |
| Interior | Soil, sand, mud or other loose residue or dirt | Should not be accepted by Depot if exhibiting these conditions. REMOVE & WASH or STEAM-CLEAN | 3.4.2 |
|  | Patch (of any size) of sticky glue | Should not be accepted by Depot if exhibiting these conditions. REMOVE | 3.4.9 |
|  | Infestation | Should not be accepted by Depot if exhibiting these conditions. REMOVE & STEAM-CLEAN | 3.4.4 |
|  | Persistent Odour | Should not be accepted by Depot if exhibiting these conditions. WASH or STEAM-CLEAN, VENTILATE | 3.4.6 |
|  | Standing water | Should not be accepted by Depot if exhibiting these conditions. REMOVE | 3.4.8 |
|  | Organic residues e.g. Blood, Meat, Fish, beans, grains, seeds etc. | Should not be accepted by Depot if exhibiting these conditions. REMOVE & WASH or STEAM-CLEAN | 3.4.2 |
|  | Cargo securing devices such as metal or wire straps, cables, chains, string, rope, tape etc | Should not be accepted by Depot if exhibiting these conditions. REMOVE | 3.4.12 |
| Floors and Walls | Transferable stains & tyre marks | REMOVE & WASH or STEAM-CLEAN | 3.4.7 |
|  | Floor Drain holes | Clean, prove clear and operating correctly | 3.4.14 |

## CLEANING CRITERIA – CONTAINERS THAT HAVE PREVIOUSLY     CONTAINED DANGEROUS, HAZARDOUS, POTENTIALLY DANGEROUS OR OBNOXIOUS CARGOES

These criteria to be applied in addition to the criteria noted in Tables 2.1 and 2.2 as applicable.

| COMPONENT | CONDITION | ACTION REQUIRED | Refer to Section |
| --- | --- | --- | --- |
| Interior And Exterior | Labels, marks or signs, Dangerous or potentially Dangerous | After cleaning labels to be REMOVED. | 3.4.1 |
|  | Contamination, Dangerous or potentially Dangerous. | If condition could be threatening to human life or health container may be rejected at gate. Otherwise container must be segregated and Consignee or ML Dangerous Cargo department contacted to establish type of contaminant and appropriate action. Do not attempt to clean until instructions are received. | 3.4.2 or 3.4.3 |
| Interior | Soil, sand, mud or other loose residue or dirt in excess of that which would generally remain after a sweep out. If contamination most likely toxic, corrosive, combustible and/or contaminated dirt has been discovered. | Should not be accepted by Depot if exhibiting these conditions. Advice via DG department should be requested or via Shipper. When necessary via DG department Plan of Approach should be initiated. Container number is required for the history and to enable quick access for retrieving information from ML system. Do not attempt to clean until instructions are received. CLEAN AS ADVISED | 3.4.1 |
|  | Persistent Odour | CLEAN & VENTILATE | 3.4.6 |

# CLEANING METHODS

## INTRODUCTION

This section contains general recommendations on cleaning including a selection of possible cleaning methods for various conditions. Consult the Definition of Terms in the Appendix if in doubt about any term.

The most economical cleaning method should be chosen which is both effective and has the least adverse environmental impact. Careful consideration should be given to selecting the proper cleaning method so that multiple cleaning of a condition is minimised.

A container that has been accepted by a depot with any condition that might be harmful to human life or health must be segregated until the condition has been established and appropriate treatment advice received. If the contamination is identified as Dangerous the cleaning depot must seek specialist advice on the correct method of cleaning. Do not attempt to clean until appropriate cleaning instructions have been received.

In cases where water wash or steam clean is required cleaning personnel should carefully check for and be aware of any spillage from previously cargo or fumigant remainder which might react violently with water and/or might have asphyxiant and/or toxic effects.

Caution must be observed when water washing or steam cleaning near electrical power supplies to avoid electric shock, electrocution and/or severe burns.

ALL safety precautions as indicated by the manufacturer must be followed when using ANY chemical treatment including, but not limited to, cleaning compounds, insecticides, fungicides, fumigants or any other chemical agent.

## PERSONAL PROTECTION EQUIPMENT

Contractors and vendors carrying out cleaning and other EMR services to MAERSK LINE are required to have an own Health, Safety and Environment Policy that covers all necessary instructions according to local and container business regulations. The lack of this Policy should be sufficient to determine an immediate cancellation of the existing contract.

## GENERAL CLEANING METHODS

Select the best and most economical method for each situation from the alternatives below. The method chosen must not have any detrimental effect on any part of the container e.g. original paint, wooden floor etc. and should have minimal adverse environmental impact:

- Sweep out.

- Vacuum clean.

- Spread absorbent powder then sweep out or vacuum clean.

- Low pressure water-wash (usually cold water, no detergent).

- Scraping or using a sanding disk or wire brush.

- Full floor sanding – not to be applied to containers fitted with “Greentech” bamboo laminate floor panels.

- High pressure water wash - recommended minimum pressure 7580 KPa (1090psi):

- Cold without detergent.

- Hot without detergent - recommended minimum temperature 45C (113F)

- Cold with detergent.

- Hot with detergent.

- Steam clean - recommended minimum pressure 7580 KPa (1090psi), minimum temperature 100C (212F):

- Without detergent.

- With Detergent.

- Spread solvents with a rag.

- Refurbishment using abrasive blasting.

- Replacement of component.

## SPECIFIC CLEANING METHODS

Following are methods recommended for cleaning specific conditions as listed in the Cleaning Criteria tables:

### Labels, Marks or Signs

A cold high-pressure water wash without detergent should be used to loosen paper labels. If this is insufficient the labels should be removed by scraping. If mechanical methods are insufficient apply solvents to the label with a rag then remove label by scraping.

- Vinyl labels should be removed by loosening the edge with a scraper and peeling off.

- Moderate heat and/or solvents may be applied to aid in loosening the label.

- Labels held on with a wire should be removed by cutting the wire and detaching the label.

### Dry Contamination (Debris or Dirt)

- Dangerous

If the contamination is known to be threatening to human life or health container should be rejected at the gate. Otherwise the container must be segregated and no 	attempt at cleaning should be made until the consignee or ML Dangerous Cargo department has been contacted, the type of contaminant identified and the appropriate method of treatment advised.

- Non-Dangerous

Sweep out or vacuum clean the container. If this is insufficient, or if the contamination resists removal by sweeping or vacuum cleaning, remove by scraping with appropriate hand tools. Application of solvents with a rag may help to loosen contaminants. Serious or widespread contamination may require removal, as a last resort, by sanding or abrasive blasting. Such action should NOT be taken unless advance approval of ML is obtained. It is not necessary to clean the entire container unless the entire surface is contaminated.

### Wet Contamination

- Dangerous

If the contamination is known to be threatening to human life or health the container involved should be rejected at the gate. Otherwise the container must be segregated and no attempt at cleaning should be made until the consignee or ML Dangerous Cargo department has been contacted, the type of contaminant identified and the appropriate method of treatment advised.

Liquids in a closed container may vaporise and form a contaminating gas. If a gas or odour is detected determine if it is Dangerous. Proceed in accordance with the repair method listed in paragraph 3.2.6

- Non-Dangerous

If a drop or pool of liquid is on the floor surface, or within a gouge, blot or wipe dry thoroughly with absorbent paper, sponge or rag. When no standing liquid remains spread an absorbent powder, capable of absorbing the type of contaminant, is to be used and sweep out or vacuum clean once the contaminant is fully absorbed.

If this fails or is not feasible use high-pressure water (hot or cold) to wash out the contaminant. If necessary add detergent to the wash water. If this is insufficient steam-clean the contaminated area. It is not necessary to clean the entire container unless the entire surface is contaminated.

### Infestation

Segregate the container and determine the type of infestation. If necessary contact the consignee or an extermination company for guidance. Remove (if possible) or neutralise the infestation using an insecticide, fungicide, fumigant or other chemical or mechanical agent. If a residue remains after the infestation has been removed, remove it in accordance with Section 3.4.2 or 3.4.3 if this is insufficient, or if a component is damaged by the infestation, replace the component. Ensure that disposal of infested components is done in a safe and sanitary manner so that the infestation can not spread and that personnel and/or the environment will not be harmed by the infestation or any poisons used in destroying the infestation. Follow all safety precautions as indicated by the manufacturer of the insecticide, fungicide, fumigant or other chemical agent used.

### Paint Contamination

Contamination should be removed using the methods outlined in Sections 3.4.2 or 3.4.3. After contaminants are removed determine whether or not the primer coat is intact. If it is, ensure that the primer coat is free from dirt, oils or solvents and re-apply topcoat. If the primer is not intact, or if its condition is uncertain, abrasive blast the metal substrate to near white metal and apply approved primer and topcoat. Repair should be restricted to affected areas only.

For more instructions, pls refer to the Guidelines to the Condition of Paintwork Damage in GLBEQUEMR enable site:

In the case of paint separation, if the separation was not caused by contamination and there is no evidence of mechanical damage, segregate the container and contact the Maersk Line EMR Operations Manager. Do not disturb the paint surface pending Maersk Line EMR Operations Manager’s guidance since a warranty claim with a paint manufacturer may ensue before repair is authorised.

### Persistent Odour

Not all odours in a container may be of a persistent nature, which require cleaning action in accordance with Table 2.1. Consult the Appendix: Definitions of Terms, to determine whether or not an odour qualifies as being persistent and therefore subject to cleaning.

If the source of the odour is known to be Dangerous or is unknown segregate the container, with the doors closed, and contact the consignee or Maersk Line Dangerous Cargo department to determine appropriate treatment. If the source is known to be non-Dangerous remove it before attempting to neutralise the odour. Use the appropriate method in Section 3.4.2, 3.4.3 or 3.4.4.

Once the source of the odour has been removed ventilate the container by opening and tying back the doors, using fans to assist ventilation if possible.

### Liquids and Transferable Stains

If a drop or pool of liquid is on the floor surface blot or wipe dry with absorbent paper, sponge or rag. After the drop or pool of liquid has been removed spread an absorbent powder on the floor and sweep out or vacuum out once fully absorbed. If that fails, or the use of absorbent powder is not appropriate, apply an emulsifying agent (such as detergent) directly then remove the residue with a sponge or a rag. If these methods are not adequate, or if the stains are extensive, use a high-pressure water wash.

### Condensation or Standing Water (and other miscellaneous wet conditions)

Mop up standing water and allow the remaining moisture to evaporate. Ventilate by opening and tying back doors using fans to speed up drying if possible. In severe cases mechanical dryers (heaters) or fans may aid evaporation.

### Glue Residues

- Sticky or Wet Glue

Sticky or wet glue may be made non-sticky by applying non-perfumed talcum powder to affected areas. Once the residues have been rendered non-sticky determine 	if further cleaning is required. If residues require being removed scraping or application of solvents can remove them.

- Non-Sticky or Dry Glue

Non-sticky or dry glue that is required to be cleaned should be prepared and painted over using owner-approved coatings. If residues require to be removed scraping or application of solvents can remove them.

### Protruding Nails

Remove nails by driving or pulling out. If resulting nail holes are over 6mm in diameter repair the hole by filling or sealing. If a nail hole is less than 6mm in diameter the hole need not be repaired unless it is not light tight. If the nail can not be removed without damaging the floor drive the nail head flush with the surface and bend the point over against the reverse side of the wooden floor. Ensure that the point does not protrude in a way that might damage objects or injure personnel.

### Graffiti

Use a cleaning solvent or owner approved cleaning product applied with a rag to remove graffiti. If the underlying paint is damaged before or during the repair, remove solvent residues; let the component dry then wipe clean and prime and topcoat. If the graffiti cannot easily be removed prepare the surface and paint over with owner-approved topcoat.

### Cargo Securing Devices including Tape

Detach and remove securing devices. If permanent components of the container are damaged by the removal repair the components.

Loosen and peel off tape using solvents or moderate heat as necessary in order to leave a clean surface. If any residue remains remove it using a solvent. Restore any damaged paint by cleaning, priming and top coating as required.

### Reefer Container Floor Drain holes

Clean drains with high-pressure water hose. Prove drains clear and operating correctly by pouring water through and observing correct drainage. If drains are not operating correctly (draining) remove cap and float ball cage and free up and clean float balls if applicable.

### Fumigation Residues

Containers that contain fumigant residues should be refused at turn-in to a depot.

If there is a requirement to clean by a contractor/depot the residues must be handled with great care and appropriate safety precautions must be taken e.g. ventilated area, NEVER storage in waste bins and/or accommodation and residues to be treated as chemical waste.

# DEFINITION OF TERMS

The following is a glossary of terms used within this cleaning guide:

Contamination (Dangerous)

Any residue, wet or dry, known to be of harmful nature or of an unknown nature that may be harmful to human life or health.

Contamination (Non-Dangerous)

Any residue, wet or dry, known not to be Dangerous. This includes cargo packaging and dunnage as well as any other material or substance that has permeated or is clinging to the container surfaces. However, stains that have permeated into the container surfaces but will not harm cargo are not to be considered contamination.

Desiccant

Substance capable of absorbing large amounts of moisture e.g. silica gel crystals.

Glue (Dry)

Glue IN which adhesive properties have expired.

Glue (Sticky)

Glue that still has adhesive properties.

Graffiti

Marks or notations applied directly to the container other than the original markings or markings applied at the direction of ML.

Dangerous Cargo Labels, Marks or Signs

Labels that are affixed to a container to warn of the presence of Dangerous cargo inside during shipment. The International Maritime Dangerous Goods Code (IDMG) requires these labels to be removed from the container after the cargo has been discharged.

Infestation

Presence of insects, rodents, fungi, other living creatures, organisms or matter (including nests).

Labels

Temporary stickers attached to the container by the user.

Odour (Persistent)

Any smell of a particular substance or of an unpleasant nature within the container that remains after the container has been vented with the doors fully open for 30 minutes then closed and re-opened at least 24 hours later. Any smell which could reasonably be expected to taint a future general cargo.

Transferable stain

Discoloration of any interior surface that adheres to the fingers when rubbed. This Does not include tyre marks and normal surface dust in GP containers.